## Participant: NUCLEAR
You are responsible for the NUCLEAR technology in the market.
In real life, a bid includes multiple energy and price segments. However, for simplicity's sake, in this game you will only offer one segment. Therefore, your bid for a specific round will consist of the following:
- The price per megawatt-hour (€/MWh) at which you are willing to sell your energy. The minimum value (floor) is 0 €/MWh. The maximum value (cap) is 180 €/MWh.
- The amount of energy you are offering (GWh). The minimum value is 0 GWh. The maximum is 10 GWh.
### Take into consideration that:
1. Your unitary variable cost associated with fuel consumption is 5 €/MWh.
2. Your don’t have CO2 emissions associated with generation.
3. Nuclear plants must work at full capacity. This means that, regardless the energy you sell in each round, your plant will deliver 10 GWh. If you sell less than that, you will pay a penalty (because you will inject more energy than that compromised in the market, thus you create an imbalance). The penalty price is different for each round, and depends on the overall imbalance, considering deviations from all participants.
For example, if you sell 8 GWh in the market, you create an imbalance of 2 GWh. If the market clearing price is 20 €/MWh:
- You earn 8x20 = 160 thousand € (market incomes).
- Since you actually generate 10 GWh, you pay 10x5 = 50 thousand € for the fuel consumption (variable cost).
- If the penalty price were 30 €/MWh, you would pay a penalty of 2x30 = 60 thousand €.
- Thus, overall, you earn 160-50-60 = 50 thousand € (total incomes).